WWVB reception tips

Several power outages due to stormy weather has reminded me of a tip to improve wwvb reception. Turn off and unplug all unused electrical appliances, especially computers, TV’s, lights with dimmers, and Microwave ovens.

For loop antennas placement of the antenna to reduce interference is preferred to aiming for the station to be received. The nulls are very sharp compared to the peaks and if the station you desire is in the direction of a strong interference source you may not receive it anyway.

If the source is local then placement of the antenna at a different location can change the geometry for the better. That is for movement in a direction perpendicular to the local interference/remote station the angle of apparent separation increases.